## Slide 1: IX. Basic Implementation Techniques and Fast Algorithm
314
Fast Algorithm Design
Goals: Saving Computational Time
Number of Additions
Number of Multiplications
Number of Time Cycles
Saving the Hardware Cost for Implementation
Saving the buffer size
Repeated Using a Structure
 9-A 快速演算法設計的原則

## Slide 2
315
Four important concepts that should be learned from fast algorithm design:
(1) N-point DFT
(2) Complexity of LTI Systems
(3) Replacement of DFTs
(4) Simplification Techniques

## Slide 3
如何簡化下面四個運算
y1 = ax1 + 2ax2
316
 9-B 對於簡單矩陣快速演算法的設計

## Slide 4
(i) z1 = a[x1 + x2], z2 = z1
(ii) z3 = (b−a)x2, z4 = (c−a)x1
(iii) y1 = z1 + z3, y2 = z2 + z4
317
(4)

## Slide 5
問題思考：如何對 complex number multiplication 來做 implementation？

## Slide 6
 9-C General Way for Simplifying Calculation
假設一個 MN sub-rectangular matrix S 可分解為 column vector 及 row vector 相乘
若 [a1, a2, …., aM]T 有 M0 個相異的 non-trivial values
(am  2k, am  2kah where m  h)
[b1, b2, …., bN] 有 N0 個相異的 non-trivial values
則 S 共需要 M0 + N0 個乘法
319

## Slide 7
Step 1 za = b1x[1] + b2x[2] + …. + bNx[N]
Step 2 z[1] = a1 za , z[2] = a2 za , ………, z[N] = aM za
320

## Slide 8
簡化理論的變型
S1 也是一個 MN matrix
若 S1 有 P1 個值不等於 0, 則 S 的乘法量上限為 M0 + N0 + P1
以此類推
321

## Slide 9
思考： 對於如下的情形需要多少乘法
322

## Slide 10
3  3 DFT 可以用特殊方法簡化
323
 9-D Examples
DFT:
Without any simplification, the DFT needs 4N2 real multiplications (x[n] may be complex)

## Slide 11
 5  5 DFT 的例子
324
real part
imaginary part

## Slide 12
8-point DCT
觀察對稱性質之後，令
325

## Slide 13
326
Part 1:

## Slide 14
[Ref] B. G. Lee, “A new algorithm for computing the discrete cosine transform,”
IEEE Trans. Acoust., Speech, Signal Processing, vol. 32, pp. 1243-1245, Dec. 1984.
327
Part 2:

## Slide 15
328
 N-point DFT:
 N-point DCT, DST, DHT:
 Two-dimensional (2-D) Nx  Ny-point DFT:
 Convolution of an M-point sequence and an N-point sequence:
when M/N and N/M are not large,
when N >> M and M is a fixed constant.
when M >> N and N is a fixed constant.
 9-E Summary of the Complexity
Why?

## Slide 16
329
 2-D Convolution of an (Mx  My )-point matrix and an (Nx  Ny )-point matrix:
when MxMy/NxNy and NxNy/MxMy are not large,
when MxMy >> NxNy
when NxNy >> MxMy , and Mx, My are fixed constants.

## Slide 17
 C. S. Burrus and T. W. Parks, “DFT / FFT and convolution algorithms”, John Wiley and Sons, New York, 1985.
 R. E. Blahut, Fast Algorithm for Digital Signal Processing, Addison Wesley Publishing Company.
N-point Fourier Transform: 運算量為 N2
FFT (with the Cooley Tukey algorithm): 運算量為 NlogN
X. Fast Fourier Transform
330
要學到的概念：(1)快速演算法不是只有 Cooley Tukey algorithm
(2) 不是只有 N = 2k 有時候才有快速演算法

## Slide 18
(1) Cooley-Tukey algorithm (Butterfly form)
(2) Radix-4, 8, 16, …. Algorithms
(3) Prime Factor Algorithm
(4) Goertzel Algorithm
(5) Chirp Z transform (CZT)
(6) Winograd algorithm
 10-A Other DFT Implementation Algorithms

## Slide 19
Reference
 J. W. Cooley and J. W. Tukey, “An algorithm for the machine computation of complex Fourier series,” Mathematics of Computation, vol. 19, pp. 297-301, Apr. 1965. (Cooley-Tukey)
 C. S. Burrus, “Index Mappings for multidimensional formulation of the DFT and convolution,” IEEE Trans. Acoustics, Speech, and Signal Processing, vol. 25, pp. 1239-242, June 1977. (Prime factor)
 G. Goertzel, “An algorithm for the evaluation of finite trigonometric series,” American Math. Monthly, vol. 65, pp. 34-35, Jan. 1958. (Goertzel)
 C. R. Hewes, R. W. Broderson, and D. D. Buss, “Applications of CCD and switched capacitor filter technology,” Proc. IEEE, vol. 67, no. 10, pp. 1403-1415, Oct. 1979. (CZT)
 S. Winograd, “On computing the discrete Fourier transform,” Mathematics of Computation, vol. 32, no. 141, pp. 179-199, Jan. 1978. (Winograd)
 R. E. Blahut, Fast Algorithm for Digital Signal Processing, Reading, Mass., Addison-Wesley, 1985.

## Slide 20
 10-B Cooley Tukey Algorithm
When N = 2k
Therefore,
one N-point DFT = two (N/2)-point DFT + twiddle factors
twiddle factors
x1[n] = x[2n], x2[n] = x[2n+1]
333
+
+
-1

## Slide 21
8-point DFT
x[0]
x[2]
x[4]
x[6]
x[1]
x[3]
x[5]
x[7]
4-point DFT
4-point DFT
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
1
w
w2
w3
-1
-1
-1
-1
334

## Slide 22
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
-1
-1
-1
-1
-1
-1
-1
-1
1
w2
1
w2
8-point DFT
1
w
w2
w3
-1
-1
-1
-1
335

## Slide 23
2k-point DFT 一共有 k 個 stages
每個 stage 和下一個 stage 之間有 2k-1 個 twiddle factors
所以，一共有 2k-1(k-1) 個 twiddle factors
一般而言，每個 twiddle factor 需要 3 個 real multiplications
 2k-point DFT 需要
 Number of real multiplications 的估算
個 real multiplications
Complexity of the N-point DFT: O(Nlog2N)
336
k-1 次 decomposition

## Slide 24
 8-point DFT 只需要 4 個 real multiplications (Why?)
 更精確的分析，使用 Cooley-Tukey algorithm 時，N-point DFT 需要
個 real multiplications
(Why?)
337

## Slide 25
 10-C Radix-4 Algorithm
限制： N = 4k
or N = 24k (此時 Cooley-Tukey algorithm 和 radix-4 algorithm 並用)
One N-point DFT = four (N/4)-point DFTs + twiddle factors
twiddle factors
338

## Slide 26
Note:
(1) radix-4 algorithm 最後可將 N = 4k-point DFT 拆解成 4-point DFTs 的組合
4-point DFTs 不需要任何的乘法
(2) 使用 radix-4 algorithm 時，N-point DFT 需要
個 real multiplications
339

## Slide 27
 Number of real multiplications for the N-point DFT
N | 乘法數 | 加法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
1 | 0 | 0 | 11 | 46 | 24 | 28 | 39 | 182
2 | 0 | 4 | 12 | 8 | 25 | 148 | 40 | 100
3 | 2 | 12 | 13 | 52 | 26 | 104 | 42 | 124
4 | 0 | 16 | 14 | 32 | 27 | 114 | 44 | 160
5 | 10 | 34 | 15 | 40 | 28 | 64 | 45 | 170
6 | 4 | 36 | 16 | 20 | 30 | 80 | 48 | 92
7 | 16 | 72 | 18 | 32 | 32 | 72 | 52 | 208
8 | 4 | 52 | 20 | 40 | 33 | 160 | 54 | 228
9 | 16 | 72 | 21 | 62 | 35 | 150 | 56 | 156
10 | 20 | 88 | 22 | 80 | 36 | 64 | 60 | 160

## Slide 28
N | 乘法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
63 | 256 | 96 | 280 | 192 | 752 | 360 | 1540
64 | 204 | 104 | 468 | 204 | 976 | 420 | 2080
66 | 284 | 108 | 456 | 216 | 1020 | 480 | 2360
70 | 300 | 112 | 396 | 224 | 1016 | 504 | 2300
72 | 164 | 120 | 380 | 240 | 940 | 512 | 3180
80 | 260 | 128 | 560 | 252 | 1024 | 560 | 3100
81 | 480 | 144 | 436 | 256 | 1308 | 672 | 3496
84 | 248 | 160 | 680 | 288 | 1160 | 720 | 3620
88 | 412 | 168 | 580 | 312 | 1324 | 784 | 4412
90 | 340 | 180 | 680 | 336 | 1412 | 840 | 4580

## Slide 29
N | 乘法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
1008 | 5356 | 1440 | 8680 | 2520 | 16540 | 4032 | 29488
1024 | 7436 | 1680 | 10420 | 2688 | 19108 | 4096 | 37516
1152 | 7088 | 2016 | 12728 | 2880 | 20060 | 4368 | 35828
1260 | 7640 | 2048 | 16836 | 3369 | 24200 | 4608 | 36812
1344 | 8252 | 2304 | 15868 | 3920 | 29900 | 5040 | 36860

## Slide 30
附錄十：論文英文常見的文法錯誤
(1) *** transform, *** equation, *** method, *** algorithm 在論文當中，當成是可數名詞，而非專有名詞 (除非是所有格的形態)。
可數名詞單數時，前面要要冠詞 (a 或 the)
Fourier transform is important for signal processing. （錯誤）
The Fourier transform is important for signal processing. （正確）
A Fourier transform is important for signal processing. （正確）
Fourier transforms are important for signal processing. （正確）
I have written the Matlab program of the Parks-McClellan algorithm （正確）
I have written the Matlab program of Parks-McClellan algorithm （錯誤）
I have written the Matlab program of Parks-McClellan’s algorithm （正確）
I have written the Matlab program of the Parks-McClellan’s algorithm （錯誤）
(2) 若是所有格的形態，不必加冠詞

## Slide 31
(3) 論文視同正式的文件，對 not, is, are 不用縮寫
aren’t （錯誤） are not （正確）
they’re （錯誤） they are （正確）
he’s （錯誤） he is （正確）
don’t （錯誤） do not （正確）
(4) Suppose, assume 後面要加關係代名詞
Suppose x is a large number. （錯誤）
Suppose that x is a large number. （正確）
(5) 每一個子句都有一個動詞，而且只有一個動詞
can’t （錯誤） cannot （正確）

## Slide 32
(6) In this paper, in this section, in this chapter 開頭的句子，應該用現在式，而非未來式
In this paper, the fast algorithm of DCT will be introduced. （錯誤）
In this paper, , the fast algorithm of DCT is introduced. （正確）
(7) 在 conclusion 當中回顧文章一內容，用過去式
(9) time domain, frequency domain 前面也加冠詞
in time domain （錯誤） in the time domain （正確）
(10) 不以 “this paper”, “section *”, “Ref. [*]” 當主詞用
This paper describes several concepts. （錯誤）
In this paper, several concepts are described. （正確）
Ref. [1] proposed the method. （錯誤）
In Ref. [1], Parks and McClellan proposed the method. （正確）
(8) 敘述所引用的論文的內容，用過去式
In [10], the number theoretic transform was proposed.

## Slide 33
(12) 寫科技論文不是寫文學作品，不要用高明、漂亮、但沒有保握的文法。
儘量用簡單而有把握的文法。
(11) 提及某個 equation 時，直接括號加數字即可
in equation (3) （錯誤） in (3) （正確）
提及某個 section, table, or figure 時，前面不加冠詞，而且常用大寫
in the section 4 （錯誤） in Section 4 （正確）
in the table 5 （錯誤） in Table 4 （正確）
(13) 科技論文英文講求「長話短說」，儘量用精簡的文字來表達意思
(14) 用字儘量避免重覆

## Slide 34
(17) 很重要的論文，投稿至國際學術期刊，又對自己的英文文法沒有十足的把握時
可以用網路上的論文編修服務，來修改文法上的錯誤
本系以及台大語言中心也經常有英文論文寫作相關的訓練課程，有志將來在學術界奮鬥的同學，可以多參與相關的課程
(15) Equations 也當成是文章的一部分，所以通常也要加標點符號
The formula of Newton’s 2nd law is
F = ma.
要加標點符號
(16) 解釋 parameters 和 symbols 時，用 where 當關係代名詞
x = 10t where x is the location of the object and t is time.