## Slide 1
 11-C 計算 Linear Convolution
But how do we implement it correctly?
How do we choose P ?
Note: When
then
FFTP: the P-point FFT
IFFTP: the P-point inverse FFT
((a))P: a 除以 P 的餘數
We know that when
then
(N points)
(M points)
(P points)

## Slide 2
Convolution 有幾種 Cases
Case 1: Both x[n] and h[n] have infinite lengths.
Case 2: Both x[n] and h[n] have finite lengths.
Case 3: x[n] has infinite length but h[n] has finite length.
Case 4: x[n] has finite length but h[n] has infinite length.

## Slide 3
Case 2: Both x[n] and h[n] have finite lengths.
x[n] 的範圍為 n  [n1, n2]，大小為 N = n2 − n1 + 1
h[n] 的範圍為 n  [k1, k2]，大小為 K = k2 − k1 + 1
y[n] 的範圍?
x[n]
h[n]
y[n]
n1
n2
k1
k2
N
K
n
n
n1+k1
n2+k2
n
N+K-1
Convolution output 的範圍以及 點數， 是學信號處理的人必需了解的常識

## Slide 4
當 n 固定時
x[n] 的範圍為 n  [n1, n2]，範圍大小為 N = n2 − n1 + 1
h[n] 的範圍為 n  [k1, k2]，範圍大小為 K = k2 − k1 + 1
什麼情況下y[n] 有值？
其中至少有一個落在 [n1, n2 ] 的範圍內

## Slide 5
n − k2
n − k1
n1
n2
x[n] 有值的範圍
n − k 的範圍
必需有交集
n 的下限為 n − k1 與 n1 相重合
n − k1 = n1, n = k1 + n1
n 的上限為 n − k2 與 n2 相重合
n − k2 = n2, n = k2 + n2
所以 y[n] 的範圍是 n  [k1 + n1 , k2 + n2]
範圍大小為 k2 + n2 − k1 − n1 + 1 = N + K − 1

## Slide 6
FFT implementation for Case 2
for n = 0, 1, 2, … , N−1
for n = N, N+1 , … , P−1 P  N + K − 1
for n = 0, 1, 2, … , K−1
for n = K, K+1 , … , P−1
for n = n1+k1 , n1+k1+1, n1+k1+2, ……., k2 + n2
i.e.,
取 output 的前面 N+K1 個點

## Slide 7
證明：
(from page 387)
由於
(h1[k'] = 0 for k K)
當
時，
因為 P  N + K − 1 , P −K+ 1  N
又 x1[n] = 0 for n  N and n < 0
所以當 時
可以簡化為
這是因為只有當 時

## Slide 8
令 k = k + k1, n = n + n1 + k1
得證

## Slide 9
Case 3: x[n] has finite length but h[n] has infinite length
x[n] 的範圍為 n  [n1, n2]，範圍大小為 N = n2 − n1 + 1
h[n] 無限長
y[n] 每一點都有值 (範圍無限大）
但我們只想求出 y[n] 的其中一段
希望算出的 y[n] 的範圍為 n  [m1, m2]，範圍大小為 M = m2 − m1 + 1
h[n] 的範圍 ?
要用多少點的 FFT ?

## Slide 10
改寫成
當n = m1
當n = m2

## Slide 11
m2−n1
有用到的 h[k] 的範圍：k  [m1 − n2, m2 − n1]
此圖為 n − s 範圍示意圖
n = m1 時 n − s 的範圍
n = m1 +1 時 n − s 的範圍
n = m1 +2 時 n − s 的範圍
n = m2 時 n − s 的範圍
m1 − n2
m1 − n1
m1−n1+1
m1−n2+1
m1−n2+2
m1−n1+2
m2−n2
(n = m1)
(n = m1+1)
(n = m1+2)
(n = m2)

## Slide 12
所以有用到的 h[k] 的範圍是 k  [m1 − n2 , m2 − n1 ]
範圍大小為 m2 − n1 − m1 + n2 + 1 = N + M − 1
FFT implementation for Case 3
for n = 0, 1, 2, … , N−1
for n = N, N + 1, N + 2, ……, P −1 P  N + M − 1
for n = 0, 1, 2, … , L−1
for n = m1, m1+1, m1+2, … , m2
注意：y[n] 只選 y1[n] 的第 N 個點到第 N+M1 個點

## Slide 13
Suppose that
x[n]: input, h[n]: the impulse response of the filter
length(x[n]) = N, length(h[n]) = M (Both of them have finite lengths)
We want to compute
, y[n] = x[n]  h[n].
The above convolution needs the P-point DFT, P  M + N  1. complexity: O(P log2P)
 11-D Relations between the Signal Length and the
Convolution Algorithm
N
M

## Slide 14
Case 1: When M is a very small integer:
Directly computing
Number of multiplications for directly computing: N  M
When 3N  M  9/2(N + M  1)log2(N + M  1), i.e., M  (3/2)log2N, (粗略估計) it is proper to do directly computing instead of applying the DFT.

## Slide 15
Example: N = 126, M = 3, (difference, edge detection)
(3/2)log2N = 10.4659
When compute the number of real multiplications explicitly,
using direct implementation: 3N  M = 1134,
using the 128-point DFT:
using the 144-point DFT:

## Slide 16
Although in usual “directly computing” is not a good idea for convolution implementation, in the cases where
(a) M is small
(b) The filter has some symmetric relation
using the directly computing method may be efficient for convolution implementation.
Example:
edge detection
h[n] = [-0.1, - 0.3, -0.6, 0, 0.6, 0.3, 0.1]
for n = -3 ~ 3

## Slide 17
Example:
smooth filter
h[n] = [0.1, 0.2, 0.4, 0.2, 0.1]
for n = -2 ~ 2

## Slide 18
Case 2: When M is not a very small integer but much less than N (N >> M):
It is proper to divide the input x[n] into several parts:
Each part has the size of L (L > M).
x[n] (n = 0, 1, …., N1)  x1[n], x2[n], x3[n], …….., xS[n]
S = N/L,   means rounding toward infinite
Section 1 x1[n] = x[n] for n = 0, 1, 2, …., L 1,
Section 2 x2[n] = x[n + L] for n = 0, 1, 2, …., L 1,
:
Section s xs[n] = x[n + (s-1)L] for n = 0, 1, 2, …., L 1,
s = 1, 2, 3, …., S
x1[n]
x2[n]
x3[n]
xS-1[n]
xS[n]

## Slide 19
length = L
length = M
It should perform the P-point FFTs 2S+1 times or 2S times
P  L+M1
Why?

## Slide 20
Suppose that the P-point DFT is applied for each section
Detail of Implementation
(1) First, determine L = P  M + 1
for n = 0, 1, 2, …., L 1,
for n = L, L+1, …., N 1
(2)
for n = 0, 1, 2, …., M 1,
for n = M, M+1, …., N 1
(3) Then calculate
s = 1, 2, 3, …., S
S = N/L
(4) Then, apply “overlapped addition”
when n < 0 and n  N

## Slide 21
運算量： 2S  [(3P/2)log2P] + 3S P S  N/L, P  L+M1
(linear with N)
何時為 optimal? 
replaced by the number of multiplications for the P-point DFT
In practice, a computer program is applied to determine the optimal L.
(理論值)

## Slide 22
M (filter length)
L (section length)

## Slide 23
P = L+M1
(3) 實際上，需要考量 P-point FFT 的乘法量必需不多
例如，根據 page 407 的方法，算出當 M = 10 時， L = 41.5439 為 optimal
但實際上，應該選 L = 39，因為此時 P = L+M1 = 48 點的 DFT 有較少的乘法量
注意：
(1) Optimal section length is independent to N
(2) If M is a fixed constant, then the complexity is linear with N, i.e.,
O(N)
比較：使用原本方法時， complexity = O((N+M-1)log2 (N+M-1))

## Slide 24
Case 3 When M has the same order as N
Case 4 When M is much larger than N
Case 5 When N is a very small integer

## Slide 25
 Sectioned Convolution for the Condition where One Sequence is Finite and the Other One is Infinite
x[n]  0 for n1  n  n2, length of x[n] = N = n2  n1 + 1,
length of h[n] is infinite, and we want to calculate y[m] for m1  m m2, M = m2  m1 + 1.
Suppose that M << N.
In this case, we can try to partition x[n] into several sections.
section 1: x1[n] = x[n] for n = n1 ~ n1 + L  1, x1[n] = 0 otherwise, section 2: x2[n] = x[n] for n = n1+ L ~ n1 + 2L  1, x2[n] = 0 otherwise,  section q: xq[n] = x[n] for n = n1+ (q1)L ~ n1 + qL  1, xq[n] = 0 otherwise,


## Slide 26
Then we perform the convolution of xq[n] * h[n] for each of the sections by the method on pages 397 and 398.
(Since the length of xq[n] is L, it requires the P-point DFT, P  L+M1.
Its complexity and the optimal section length can also be determined by the formulas on page 407.

## Slide 27
 11-E Recursive Method for Convolution Implementation
u[n]: unit step function
Only two multiplications required for calculating each output.

## Slide 28
h[n] = 0.250.6|n|

## Slide 29
12. Fast Algorithm 的補充
 12-A Discrete Fourier Transform for Real Inputs
DFT:
當 f [n] 為 real 時， F [m] = F*[N − m] *: conjugation

## Slide 30
若我們要對兩個 real sequences f1[n] ，f2[n] 做 DFTs
Step 1: f3[n] = f1[n] + j f2[n]
Step 2: F3[m] = DFT{f3[n]}
Step 3:
只需一個 DFT
證明：由於 DFT 是一個 linear operation
又
F1 [m] = F1*[N − m]
F2 [m] = F2*[N − m]

## Slide 31
同理，當兩個 inputs 為
(1) pure imaginary
(2) one is real and another one is pure imaginary
時，也可以用同樣的方法將運算量減半

## Slide 32
若 input sequence 為 odd and real，
則乘法量可減為 1/4
若 input sequence 為 even f[n] = f[N-n]，
則 DFT output 也為 even F[n] = F[N-n]
若 input sequence 為 odd f[n] = -f[N-n]，
則 DFT output 也為 odd F[n] = -F[N-n]

## Slide 33
If it is known that the IDFTs of F1[m] and F2[m] are real, then the IDFTs of F1[m] and F2[m] can be implemented using only one IDFT:
[Corollary 1]
(Step 1) F3[m] = F1[m] + j F2[m]
(Step 2) f3[n] = IDFT{F3[m]}
(Step 3) f1[n] = Re{f3[n]}, f2[n] = Im{f2[n]},
[Corollary 2]
When x[n] and h[n] are both real, the computation loading of the convolution (or the sectioned convolution) of x[n] and h[n] can be halved.

## Slide 34
一般的 linear operation:
(習慣上，把 k[m, n] 稱作 “kernel”)
n = 0, 1, …., N 1, m = 0, 1, …., M 1
可以用矩陣 (matrix) 來表示
運算量為 MN
若為 linear time-invariant operation:
k[m, n] = h[m  n] (dependent on m, n 之間的差)
n = 0, 1, …., N 1, m = 0, 1, …., M 1
m  n 的範圍： 從 1N 到 M 1， 全長 M + N  1
運算量為 Llog2L, L  M+2N  2
420
 12-B Converting into Convolution

## Slide 35
大致上，變成 convolution 後 總是可以節省運算量
例子A
可以改寫為
(注意，最後一項為 convolution)
運算量為 2N + Llog2L
例子B Linear Canonical Transform
421

## Slide 36
通則：
當k[m, n] 可以拆解成 A[m]  B[m−n]  C[n]
或
即可以使用 convolution

## Slide 37
 12-C LUT
道理和背九九乘法表一樣
記憶體容量夠大時可用的方法
Problem: memory requirement
wasting energy
LUT (lookup table)
九九乘法表的例子

## Slide 38
附錄十二 創意思考
New ideas 聽起來偉大，但大多是由既有的 ideas 變化而產生
(1) Combination
(2) Analogous
(3) Connection
(4) Generalization
(5) Simplification
(6) Reverse
註：感謝已過逝的李茂輝教授，他開的課「創造發明工程」，
讓我一生受用無窮
(7) Key Factor Analysis
(8) 胡思亂想，純粹意外

## Slide 39
(7) Key Factor
(8) Imagination
(9) 純粹意外

## Slide 40
(1) Combination
A (existing)
B (existing)
C (innovation)
蒸汽機
(2) Analog
A (existing)
B (existing)
C (existing)
D (innovation)
車
火車
例：
例：
continuous
Fourier
transform
continuous
cosine
transform
discrete
Fourier
transform
discrete
cosine
transform

## Slide 41
(3) Connection
A (existing)
B (existing)
C (innovation)
例：
(4) Generalization
A (existing)
B (innovation)
保留某些特性
將其他特性推廣化
例：
Walsh transform
保留不需乘法
將 1 推廣為2k
Jacket transform
古典物理學
未能解釋的光學現象
相對論

## Slide 42
(5) Simplification
A (existing)
B (innovation)
保留某些特性
去除複雜化的因素
DFT
例：
保留 orthogonal, 正負號變化
去除
無理數乘法
Walsh transform
(6) Reverse
A (existing)
B (existing)
C (existing)
D (innovation)
電
電生磁
磁
磁生電
(安培定律)
(法拉第定律)

## Slide 43
(1) 研究問題的第一步，往往是先想辦法把問題簡化
如果不將複雜的經濟問題簡化成二維供需圖，經濟學也就無從發展起來
如果不將電子學的問題簡化常小訊號模型，電子電路的許多問題都將難以解決
個人在研究影像處理時，也常常先針對 size 很小，且較不複雜的影像來做處理，成功之後再處理 size 較大且較複雜的影像
問題簡化之後，才比較容易對問題做分析，並提出改良之道
(2) 如果有好點子，趕快用筆記下來，
好點子是很容易稍縱即逝而忘記的。
(3) 練習多畫系統圖
系統圖畫得越多，越容易發現新的點子
個人做研究時，關於發明創造的心得

## Slide 44
(4) 其實，對台大的同學而言，提出 new ideas 並不難，但是要把 ideas 變成有用的、成功的 ideas，不可以缺少分析和解決問題的能力
很少有一個 new idea 一開始就 works well for any case，任何一個成功的創意，都是經由問題的分析，解決一連串的技術上的問題，才產生出來的
(5) 當心情放鬆時，想像力特別強，有助於發現意外的點子。
(6) 就短期而言，技術性的問題固然重要
但是就長期而言，不要因為技術上的困難，而否定了一個偉大的構想

## Slide 45
大學以前的教育，是學習前人的智慧結晶
研究所的教育，是訓練創造發明和解決問題的能力

## Slide 46
問題思考
如果要濾掉高頻的雜訊，先做 DFT，再將高頻的部分都變成 0 再做 inverse DFT 不就行了？
那麼…..為什麼要用有點複雜的 FIR filter?
for m ≦ m0 and m ≧ N – m0
for m0 < m < N – m0