## Slide 1: XIV. Number Theoretic Transform (NTT)
Number Theoretic Transform and Its Inverse
Note：
(1) M is a prime number , (mod M): 是指除以 M 的餘數
(2) N is a factor of M−1
(Note: when N  1, N must be prime to M)
(3) N−1 is an integer that satisfies (N−1)N mod M = 1
(When N = M −1, N−1 = M −1)
 14-A Definition

## Slide 2
When α satisfies the above equations and N = M −1, we call α the “primitive root”.
(4) α is a root of unity of order N
的求法與 N−1 相似
is an integer that satisfies mod M = 1

## Slide 3
Example 1:
M = 5  = 2 1 = 2 (mod 5) 2 = 4 (mod 5) 3 = 3 (mod 5) 4 = 1 (mod 5)
When N = 4
When N = 2

## Slide 4
M = 7 , N = 6 :  cannot be 2 but can be 3.
 = 2: 1 = 2 (mod 7) 2 = 4 (mod 7) 3 = 1 (mod 7)
 = 3: 1 = 3 (mod 7) 2 = 2 (mod 7) 3 = 6 (mod 7)
4 = 4 (mod 7) 5 = 5 (mod 7) 6 = 1 (mod 7)
Example 2:

## Slide 5
Advantages of the NTT:
Disadvantages of the NTT:

## Slide 6
 14-B 餘數的計算
(1) x (mod M) 的值，必定為 0 ~ M −1 之間
(2) a + b (mod M) = {a (mod M) + b (mod M)} (mod M)
例： 78 + 123 (mod 5) = 3 + 3 (mod 5) = 1
(Proof): If a = a1M + a2 and b = b1M + b2 , then
a + b = (a1 + b1)M + a2 + b2
(3) a  b (mod M) = {a (mod M)  b (mod M)} (mod M)
例： 78  123 (mod 5) = 3  3 (mod 5) = 4
(Proof): If a = a1M + a2 and b = b1M + b2 , then
a  b = (a1 b1M + a1b2 + a2b1)M + a2b2

## Slide 7
在 Number Theory 當中
只有 M2 個可能的加法， M2 個可能的乘法
可事先將加法和乘法的結果存在記憶體當中
需要時再 “LUT”
LUT : lookup table

## Slide 8
 14-C Properties of Number Theoretic Transforms
P.1) Orthogonality Principle
proof ：
P.2) The NTT and INTT are exact inverse
proof ：

## Slide 9
P.3) Symmetry
f(n) = f(Nn) F(k) = F(Nk)
f(n) = f(Nn) F(k) = F(Nk)
NTT
NTT
P.4) INNT from NTT
 Algorithm for calculating the INNT from the NTT
(1) F(-k) : time reverse
F0, F1, F2, …, FN-1 F0, FN-1, …, F2, F1
(2) NTT[ F(k) ]
(3) 乘上
time
reverse

## Slide 10
P.5) Shift Theorem
P.6) Circular Convolution (the same as that of the DFT)
P.7) Parseval’s Theorem

## Slide 11
P.8) Linearity
P.9) Reflection
If then

## Slide 12
 If N (transform length) is a power of 2, then the radix-2 FFT butterfly algorithm can be used for efficient calculation for NTT.
Decimation-in-time NTT
Decimation-in-frequency NTT
 The prime factor algorithm can also be applied for NTTs.
 14-D Efficient FFT-Like Structures for Calculating NTTs

## Slide 13
where
One N-point NTT Two (N/2)-point NTTs
plus twiddle factors

## Slide 14
α0=1
α2=4
α0
α2
α0=1
α1=2
α2=4
α3=3
Bit
reversal
Original sequence f(n) = (1, 2, 0, 0) N = 4, M = 5
Permutation (1, 0, 2, 0)
After the 1st stage (1, 1, 2, 2)
After the 2nd stage F(k) = (3, 0, 4, 2)

## Slide 15
Inverse NTT by Forward NTT :
1) 1/N
2) Time reversal
3) permutation
4) After first stage
5) After 2nd stage
α0=1
α2=4
α0
α2
α0=1
α1=2
α2=4
α3=3
Time
reversal
Permutation

## Slide 16
 14-E Convolution by NTT
假設 x[n] = 0 for n < 0 and n  K, h[n] = 0 for n < 0 and n  H
要計算 x[n]  h[n] = z[n]
且 z[n] 的值可能的範圍是 0  z[n] < A (more general, A1  z[n] < A1 + T)
(1) 選擇 M (the prime number for the modulus operator), 滿足
(a) M is a prime number, (b) M  max(H+K, A)
(2) 選擇 N (NTT 的點數), 滿足
(a) N is a factor of M1, (b) N  H+K 1
(3) 添 0: x1[n] = x[n] for n = 0, 1, ……, K 1, x1[n] = 0 for n = K, K +1, ……., N1
h1[n] = h[n] for n = 0, 1, ……, H 1, h1[n] = 0 for n = H, H +1, ……., N 1

## Slide 17
(4) X1[m] = NTTN,M{x1[n]}, H1[m] = NTTN,M {h1[n]}
NTTN,M 指 N-point 的 DFT (mod M)
(5) Z1[m] = X1[m]H1[m], z1[n] = INTTN,M {Z1[m]},
(6) z[n] = z1[n] for n = 0, 1, …., H+K  1
(移去 n = H+K, H+K+1, …… N 1 的點)
(More general, if we have estimated the range of z[n] should be
A1  z[n] < A1 + T, then
z[n] = ((z1[n] − A1))M + A1

## Slide 18
適用於 (1) x[n]，h[n]皆為整數
(2) Max(z[n]) − min(z[n]) < M 的情形。
Consider the convolution of (1, 2, 3, 0) * (1, 2, 3, 4)
Choose M = 17, N = 8，結果為：

## Slide 19
 Max(z[n]) − min(z[n]) 的估測方法
假設 x1  x[n]  x2,
則
(Proof):
where h1[m] = h[m] when h[m] > 0 , h1[m] = 0 otherwise
h2[m] = h[m] when h[m] < 0 , h2[m] = 0 otherwise

## Slide 20
Fermat Number :
  P = 0, 1, 2, 3, 4, 5, …..
M = 3, 5, 17, 257, 65537, …
Mersenne Number : M = 2p − 1
P = 1, 2, 3, 5, 7, 13, 17, 19
M = 1, 3, 7, 31, 127, 8191, …..
If M = 2p − 1 is a prime number, p must be a prime number.
However, if p is a prime number, M = 2p − 1 may not be a prime number.
 14-F Special Numbers

## Slide 21
The modulus operations for Mersenne and Fermat prime numbers are very easy for implementation.
2k  1
Example: 25 mod 7
a = −1
100

## Slide 22
The integer field ZM can be extended to complex integer field
If the following equation does not have a sol. in ZM
無解
This means (-1) does not have a square root
When M = 4k +1, there is a solution for x2 = −1 (mod M).
When M = 4k +3, there is no solution for x2 = −1 (mod M).
For example, when M = 13, 82 = −1 (mod 13).
21 = 2, 22 = 4, 23 = 8, 24 = 3, 25 = 6, 26 = 12 = −1,
27 = 11, 28 = 9, 29 = 5, 210 = 10, 211 = 7, 212 = 1
When M = 11, there is no solution for x2 = −1 (mod M).
 14-G Complex Number Theoretic Transform (CNT)

## Slide 23
Then, “i” will play a similar role over finite field ZM such that plays over the complex field.
If there is no solution for x2 = −1 (mod M), we can define an imaginary number i such that
i2 = −1 (mod M)

## Slide 24
NTT 適合作 convolution
但是有不少的限制
新的應用： encryption (密碼學)
CDMA
 14-H Applications of the NTT

## Slide 25
References:
(1) R. C. Agavard and C. S. Burrus, “Number theoretic transforms to implement fast digital convolution,” Proc. IEEE, vol. 63, no. 4, pp. 550- 560, Apr. 1975.
(2) T. S. Reed & T. K Truoay, ”The use of finite field to compute convolution,” IEEE Trans. Info. Theory, vol. IT-21, pp.208-213, March 1975
(3) E.Vegh and L. M. Leibowitz, “Fast complex convolution in finite rings,” IEEE Trans ASSP, vol. 24, no. 4, pp. 343-344, Aug. 1976.
(4) J. H. McClellan and C. M. Rader, Number Theory in Digital Signal Processing, Prentice-Hall, New Jersey, 1979.
(5) 華羅庚, “數論導引”, 凡異出版社, 1997。

## Slide 26
許多儀器(甚至包括智慧型手機) 都有配置三軸加速器
可以用來判別一個人的姿勢和動作
附錄十四 3-D Accelerometer 的簡介
3-D Accelerometer: 三軸加速器，或稱作加速規
註：Gyrator (陀螺儀) 可以用來量測物體旋轉之方向，可補 3-D Accelerometer 之不足，許多儀器 (包括智慧型手機) 也內建陀螺儀之裝置， 3-D Accelerometer Signal Processing 和 gyrator signal processing 經常並用

## Slide 27
x-axis
y-axis
z-axis
根據 x, y, z 三個軸的加速度的變化，來判斷姿勢和動作
平放且靜止時， z-axis 的加速度為 –g = – 9.8

## Slide 28
y-axis
z-axis
y-axis
z-axis
y: 0
z: -9.8
y: -9.8sin θ
z: -9.8cos θ
tilted by θ
可藉由加速規傾斜的角度，來判斷姿勢和動作

## Slide 29
例子：若將加速規放在腳上…………….
走路時，沿著其中一個軸的加速度變化

## Slide 30
應用： 動作辨別 (遊戲機)
運動 (訓練，計步器)
醫療復健，如 Parkinson 患者照顧，傷患復原情形
其他 (如動物的動作，機器的運轉情形的偵測)
3-D Accelerometer Signal Processing 是訊號處理的重要課題之一
一方面固然是因為應用多，另一方面， 3-D Accelerometer Signal 容易受 noise 之干擾，要如何藉由 3-D Accelerometer Signal 來還原動作以及移動速度，仍是個挑戰