## Slide 1
2. Digital Filter Design (A)
任何可以用來去除 noise 作用的 operation，皆被稱為 filter
甚至有部分的 operation，雖然主要功用不是用來去除 noise，但是可以用 FT + multiplication + IFT 來表示，也被稱作是 filter
convolution
=
Reference
[1] A. V. Oppenheim and R. W. Schafer, Discrete-Time Signal Processing, London: Prentice-Hall, 3rd ed., 2010.
[2] D. G. Manolakis and V. K. Ingle, Applied Digital Signal Processing, Cambridge University Press, Cambridge, UK. 2011.
[3] B. A. Shenoi, Introduction to Digital Signal Processing and Filter Design, Wiley-Interscience, N. J., 2006.
[4] A. A. Khan, Digital Signal Processing Fundamentals, Da Vinci Engineering Press, Massachusetts, 2005.

## Slide 2
 2-A Classification for Filters
filter
digital filter
analog filter
IIR (infinite impulse response)
FIR (finite impulse response)
bilinear transform
impulse invariant
step invariant
(1) MSE (mean square error)
(2) Minimax (minimize the maximal error)
(3) frequency sampling
others
(4) others
由設計方法分類
由 response 是否 有限長分類
由 數位類比分類
關心平均誤差
最小化最大誤差

## Slide 3
Classification for filters (依型態分)
pass-stop filter
high pass filter
all pass filter
band pass filter
band stop filter
low pass filter
Wiener filter
matched filter
equalizer filter
others
Hilbert transform
differentiation
integration
smoother
edge detection
Notch filter
0
Kalman filter
particle filter

## Slide 4
FIR filter: impulse response is nonzero at finite number of points
h[n] = 0 for n < 0 and n  N
 FIR is more popular because its impulse response is finite.
(h[n] has N points, N is a finite number)
2-B FIR Filter Design
h[n]

## Slide 5
h[-1] h[0] h[1] h[k-2] h[k-1] h[k] h[k+1] h[k+2] h[N-2] h[N-1] h[N] h[N+1]
r[-k-1] r[-k] r[-k+1] r[-2] r[-1] r[0] r[1] r[2] r[k-1] r[k] r[k+1] r[k+2]
s[0] s[1]/2 s[2]/2 s[k-1]/2 s[k]/2
(a) r[n] = h[n + k], where k = (N1)/2.
Specially, when h[n] is even symmetric
h[n] = h[N−1 −n]
and N is an odd number
(b) s[0] = r[0], s[n] = 2r[n] for 0 < n  k.
(假設一)
(假設二)

## Slide 6
Impulse Response of the FIR Filter:
h[n] (h[n]  0 for 0  n  N1) r[n] = h[n + k], k = (N1)/2 (r[n]  0 for -k  n  k, see page 41)
Suppose that the filter is even, r[n] = r[n].
Set s[0] = r[0], s[n] = 2r[n] for n  0.
Then, the discrete-time Fourier transform of the filter is
(F = f t is the normalized frequency)
See page 22

## Slide 7
(1) least MSE (mean square error) form
(關心 平均 誤差)
MSE = , fs: sampling frequency
H(f): the spectrum of the filter we obtain Hd(f): the spectrum of the desired filter
(2) mini-max (minimize the maximal error) form (關心 最大 誤差)
maximal error:
The transition band is always ignored
2-C Least MSE Form and Minimax Form FIR Filters

## Slide 8
Example: desired output Hd(F)
(A) larger MSE, but smaller maximal error
(B) smaller MSE, but larger maximal error
F

## Slide 9
Generalization for Mini-Max Sense by weight function
maximal error:
weighted maximal error:
where W(f) is the weight function.
The weight function is designed according to which band is more important.
f
passband
stopband
Hd(f)
transition band
Q: How do we choose W(f) When SNR ?

## Slide 10
Example: If we treat the passband the same important as the stopband.
W(f) = 1 in the passband, W(f) = 1 in the stopband
Q1: W(f) = 1 in the passband, W(f) < 1 in the stopband 代表什麼？
Q2: W(f) < 1 in the passband, W(f) = 1 in the stopband 代表什麼？
Q4: Weighting function 的概念可否用在 MSE sense ？
Q3: 如何用來壓縮特定區域 (如 transition band 附近) 的 error？

## Slide 11
2-D Review: FIR Filter Design in the MSE Sense
F = f / fs

## Slide 12
From the facts that
when n  ,
when n = , n  0,
when n = , n = 0.
Therefore,
for n  0.

## Slide 13
Minimize MSE  Make for all n’s
 , .
Finally, set h[k] = s[0],
h[k+n] = s[n]/2, h[k  n] = s[n]/2 for n = 1, 2, 3, …., k,
h[n] = 0 for n < 0 and n  N.
Then, h[n] is the impulse response of the designed filter.

## Slide 14
 2-E FIR Filter Design in the Mini-Max Sense
References
[1] T. W. Parks and J. H. McClellan, “Chebychev approximation for nonrecursive digital filter-linear phase”, IEEE Trans. Circuit Theory, vol. 19, no. 2, pp. 189-194, March 1972.
[2] J. H. McClellan, T. W. Parks, and L. R. Rabiner “A computer program for designing optimum FIR linear phase digital filter”, IEEE Trans. Audio- Electroacoustics, vol. 21, no. 6, Dec. 1973.
[3] F. Mintz and B. Liu, “Practical design rules for optimum FIR bandpass digital filter”, IEEE Trans. ASSP, vol. 27, no. 2, Apr. 1979.
It is also called“Remez-exchange algorithm”
or “Parks-McClellan algorithm”

## Slide 15
Suppose that:
 Filter length = N, N is odd, N = 2k+1.
 Frequency response of the desired filter: Hd(F) is an even function
(F is the normalized frequency)
 The weighting function is W(F)
Two constraints

## Slide 16
用Mini-Max方法所設計出的filters，一定會滿足以下二個條件
(1) 有k+2個以上的extreme points
(2) 在extreme points上， 是定值
的情形
T. W. Parks and J. H. McClellan, “Chebychev approximation for nonrecursive digital filter-linear phase”, IEEE Trans. Circuit Theory, vol. 19, no. 2, pp. 189-194, March 1972.
證明可參考
Error 的 local maximal
local minimum

## Slide 17
:
:
(Step 1): Choose arbitrary k+2 extreme frequencies in the range of
0  F  0.5, (denoted by F0, F1, F2, ….., Fk+1)
Note: (1) Exclude the transition band.
(2) The extreme points cannot be all in the stop band.
Set E1 (error)  
Extreme frequencies: the locations where the error is maximal.
(參考 page 52)
Step1
Step2
Step5
Step3
Step4
Step6

## Slide 18
(Step 2): From page 42, [R(Fm)  Hd(Fm)]W(Fm) = (1)m+1e (where m = 0, 1, 2, ….. , k+1) can be written as
where m = 0, 1, 2, ….. , k+1.
Expressed by the matrix form:
Solve s[0], s[1], s[2], ….. , s[k] from the above matrix
(performing the matrix inversion).
Square matrix

## Slide 19
(Step 3): Compute err(F) for 0  F  0.5, exclude the transition band.
(Step 4): Find k+2 local maximal (or minimal) points of err(F)
local maximal point: if q() > q( + ) and q() > q(  ),
then  is a local maximal of q(x).
local minimal point: if q() < q( + ) and q() < q(  ),
then  is a local minimal of q(x).
Other rules: Page 58
Denote the local maximal (or minimal) points by
These k+2 extreme points could include the boundary points of the transition band

## Slide 20
(Step 5):
Set E0 = Max(|err(F)|).
(Case a) If E1  E0 > , or E1  E0 < 0 (or the first iteration) 
set Fn = Pn and E1 = E0, return to Step 2.
(Case b) If 0  E1  E0    continue to Step 6.
(Step 6):
Set h[k] = s[0],
h[k+n] = s[n]/2, h[k  n] = s[n]/2 for n = 1, 2, 3, …., k
(referred to page 41)
Then h[n] is the impulse response of the designed filter.

## Slide 21
 2-F Mini-Max FIR Filter 設計時需注意的地方
57
(1) Extreme points 不要選在 transition band
Initial guess的extreme points只要注意別取在transition band裡，即能保證 converge，不同的guess會影響converge的速度但不影響結果
(2) E1 (error of the previous iteration) < E0 (present error) 時，亦不為收斂
(3) 思考： page 53 中的 matrix operation，如何用一行的指令寫出？

## Slide 22
(4) Extreme points 判斷的規則：
(a) The local peaks or local dips that are not at boundaries must be extreme points.
boundaries: F = 0, F = 0.5, 以及 transition band 的兩端
(b) For boundary points
58
F = 0
F = 0
Hd(F)
Add a zero to the outside and conclude whether the point is a local maximum or a local minimum.

## Slide 23
59
(5) 有時，會找到多於 k+2 個 extreme points, 該如何選
(a) 優先選擇不在 boundaries 的 extreme points
(b) 其次選擇 boundary extreme points 當中 |err(F)| 較大的，
直到湊足 k+2 個 extreme points 為止
(c) 在 boundary extreme points 的 |err(F)| 一樣大的情形，
優先選擇 transition bands 兩旁的點

## Slide 24
 2-G Examples for Mini-Max FIR Filter Design
Example 1: Design a 9-length highpass filter in the mini-max sense
ideal filter: Hd(F) = 0 for 0  F < 0.25,
Hd(F) = 1 for 0.25 < F  0.5,
transition band: 0.22 < F < 0.28  = 0.001
weighting function: W(F) = 0.25 for 0  F  0.22,
W(F) = 1 for 0.28  F  0.5,
(Step 1) Since N = 9, k = (N-1)/2 = 4, k+2 = 6,
 Choose 6 extreme frequencies
(e.g., F0 = 0, F1 = 0.1, F2 = 0.2, F3 = 0.3, F4 = 0.4, F5 = 0.5)
[R(Fn) Hd(Fn)]W(Fn) = (1)n+1e, n = 0, 1, 2, 3, 4, 5.

## Slide 25
(Step 2)

## Slide 26
R(F) = 0.5120 – 0.6472cos(2F) – 0.0297cos(4F) + 0.2472cos(6F)
+ 0.0777cos(8F)
(Step 3) err(F) = [R(F) – Hd(F)]W(F)
err(F)
s [0]
s [1]
s [2]
s [3]
s [4]
W[F] = 0 for 0.22 < F < 0.28

## Slide 27
(Step 4) Extreme points:
F0 = 0, F1 = 0.125, F2 = 0.22, F3 = 0.28, F4 = 0.356, F5 = 0.5
(Step 5) E0 = Max[|err(F)|] = 0.1501, return to Step 2.
Second iteration
(Step 2) Using F0 = 0, F1 = 0.125, F2 = 0.22, F3 = 0.28, F4 = 0.356, F5 = 0.5
 s[0] = 0.5018, s[1] = –0.6341, s[2] = –0.0194, s[3] = 0.3355, s[4] = 0.1385
(Step 3) err(F) = [R(F) – Hd(F)]W(F),
(Step 4) extreme points : 0, 0.132, 0.22, 0.28, 0.336, 0.5
(Step 5) E0 = Max[|err(F)|] = 0.0951, return to Step 2.

## Slide 28
Third iteration
(Step 2), (Step 3), (Step 4), peaks : 0, 0.132, 0.22, 0.28, 0.334, 0.5
(Step 5) E0 = 0.0821, return to Step 2.
Fourth iteration
(Step 2), (Step 3) , (Step 4), peaks : 0, 0.132, 0.22, 0.28, 0.334, 0.5
(Step 5) E0 = 0.0820, E1  E0 = 0.0001  , continues to Step 6.

## Slide 29
(Step 6) From s[0] = 0.4990, s[1] = –0.6267, s[2] = –0.0203, s[3] = 0.3316, s[4] = 0.1442
h[4] = s[0] = 0.4990, h[3] = h[5] = s[1]/2 = –0.3134,
h[2] = h[6] = s[2]/2 = –0.0101, h[1] = h[7] = s[3]/2 = 0.1658,
h[0] = h[8] = s[4]/2 = 0.0721.

## Slide 30
Example 2: Design a 7-length digital filter in the mini-max sense
ideal filter: Hd(F) = 1 for 0  F < 0.24,
Hd(F) = 0 for 0.24 < F  0.5, transition band: 0.21 < F < 0.27
weighting function: W(F) = 1 for 0  F  0.21,
W(F) = 0.5 for 0.27  F  0.5,
(Step 1) Since N = 7, k = (N-1)/2 = 3, k+2 = 5,  Choose 5 extreme frequencies
(e.g., F0 = 0.05, F1 = 0.15, F2 = 0.3, F3 = 0.4, F4 = 0.5)

## Slide 31
(Step 2)
 s[0] = 0.4638, s[1] = 0.6327, s[2] = 0.0809, s[3] = -0.1608, e = -0.0364
R(F)

## Slide 32
After Step 2,
(Step 3) err(F)
(Step 4) extreme points: 0.089, 0.21, 0.27, 0.369, 0.5.
(Step 5) E0 = Max[|err(F)|] = 0.3396, return to Step 2.
Iteration | 1 | 2 | 3 | 4 | 5 | 6 | 7
Max[¦err(F)¦] | 0.3396 | 0.2371 | 0.3090 | 0.1944 | 0.1523 | 0.1493 | 0.1493

## Slide 33
After 7 times of iteration
s[0] = 0.4243, s[1] = 0.7559, s[2] = -0.0676, s[3] = -0.2619, e = 0.1493
(Step 6):
h[3] = 0.4243, h[2] = h[4] = s[1]/2 = 0.3780,
h[1] = h[5] = s[2]/2 = -0.0338,
h[0] = h[6] = s[3]/2 = -0.1309, h[n] = 0 for n < 0 and n > 6

## Slide 34
附錄二：Spectrum Analysis for Sampled Signals
Basic rule：把間隔由 1 換成 fs /N where fs = 1/ t
已知 x[n] 是由一個 continuous signal y(t) 取樣而得
x[n] = y(nt)
DFT: FT:
Q: x[n] 的 DFT 和 y(t) 的 Fourier transform 之間有什麼關係？
(學信號處理的人一定要會的基本常識)
(Very important)

## Slide 35
fs = 1/ t
for m  N/2
for m > N/2
0 fs/2 fs
0 N/2 N
frequency
m:
(1)
(2)
(2)
(1)

## Slide 36
Proof：
用 t = nt, f = mf 代入
當
i.e.,

## Slide 37
Example：已知
y(t) = (2t)2 for 0  t  1
如何用 DFT 來正確的畫出 y(t) 的頻譜？
y(t) = (4－2t)2 for 1  t  2
取樣間隔： t = 0.1
x[n] = y(n t) for 0  n  20

## Slide 38
(Step 1) Perform the DFT for x[n]
x[n] = y(n t) for 0  n  20
N = 21

## Slide 39
(Step 2-1)
for m  N/2
for m > N/2
In this example,
(Step 2-2)
y(t) 的頻譜