## Slide 1
 Suppose that we want:
 passband ripple  1,
 stopband ripple  2,
 width of transition band  F (expressed by normalized frequency)
F = (f1  f2)/fs = (f1  f2)T (fs: sampling frequency, T: sampling interval)
Then, the estimated length N of the digital filter is:
.
When there are two transition bands, F = min(F1, F2)
犧牲 transition band 的 frequency response, 換取較高的 passband and stopband accuracies
 2-H Relations among Filter Length N, Transition Band, and Accuracy

## Slide 2
[Ref] F. Mintzer and L. Bede, “Practical design rules for optimum FIR bandpass digital filter”, IEEE Trans. ASSP, vol. 27, no. 2, pp. 204-206, Apr. 1979.
問題：假設 1 = 2 =  ，N 為固定，
當 F 變為 A 倍時，  變為多少？

## Slide 3
N = 17, k+2=10
transition band: 0.24 ~ 0.26
N = 17,
transition band: 0.2 ~ 0.3
boundary of transition band

## Slide 4
If we treat the passband more important than the stop band
W(f) = 1 in the passband, 0 < W(f) < 1 in the stopband
If we treat the stop band more important than the pass band
0 < W(f) < 1 in the passband, W(f) = 1 in the stopband
 2-I Relations between Weight Functions and Accuracy

## Slide 5
Larger error near the transition band
Hd(F)
H(F)

## Slide 6
 2-J FIR Filter in MSE Sense with Weight Functions
F = f / fs
可對照 pages 47~49
問題：
when n  
n = 0 ~ k
(not orthogonal)

## Slide 7
τ = 0 ~ k, n = 0 ~ k
可以表示成 (k+1)  (k+1) matrix operation
B S = C
S = B−1C
τ = 0
τ = 1
τ = 2
τ = k
n = 0
n = 1
n = 2
n = k

## Slide 8
Think： Is it possible to apply the transition band to the FIR filter in the MSE sense?

## Slide 9
 2-K Four Types of FIR Filter
 Type 1
h[n1] = h[n2 − n] and N is odd.
(even symmetric)
點數為 N
h[n] = 0 for n < 0 and n  N
k = (N1)/2
之前的方法只討論到Type 1

## Slide 10
 Type 1:
 Type 2:
h[n] = h[N−1− n] (even symmetric) and N is odd.
h[n] = h[N−1− n] (even symmetric) and N is even.
 Type 3:
h[n] = −h[N−1− n] (odd symmetric) and N is odd.
 Type 4:
h[n] = −h[N−1− n] (odd symmetric) and N is even.
k = (N−1)/2

## Slide 11
 Type 2: When h[n] = h[N−1− n] and N is even: (even symmetric)
令 r[n] = h[n + k], where k = (N1)/2
(注意此時 k 不為整數)
h[0] h[1] h[k-3/2] h[k-1/2] h[k+1/2] h[k+3/2] h[N-2] h[N-1]
r[-k] r[-k+1] r[-3/2] r[-1/2] r[1/2] r[3/2] r[k-1] r[k]
s[1]/2 s[2]/2 s[k-1/2]/2 s[k+1/2]/2
(比較 page 41)

## Slide 12
當
設計出 s[n] 之後
r[n] = s[n+1/2]/2, h[n] = r[n − k],
n = 1, 2, …, k+1/2

## Slide 13
Design Method for Type 2
由於 n 和 n+1 兩項相加可得
所以可以「判斷」 R(F) 能被改寫成
求 s1[n] 和 s[n] 之間的關係

## Slide 14
(令 k1 + 1/2 = k)
比較係數可得
for n = 2, 3, …., k−1/2

## Slide 15
只需將 pages 53-56 的方法當中，Hd(F) 換成
W(F) 換成
k 換成 k − 1/2 = N/2 − 1
注意 s1[n] 和 s[n] 之間的關係即可

## Slide 16
Design Method for Type 3
由於 n−1 和 n+1 兩項相減可得
所以「判斷」可將 R(F) 改寫為

## Slide 17
令 k1 = k − 1, 比較係數可得
for n = 2, 3, …., k−2

## Slide 18
將 pages 53-56 的方法當中，Hd(F) 換成
W(F) 換成
k 換成 k − 1
注意s1[n] 和 s[n] 之間的關係即可
Think：Design Method for Type 4

## Slide 19
附錄三：Matlab 寫程式需注意的地方
(1) 迴圈能避免就儘量避免
(2) 儘可能使用 Matrix 及 Vector operation
Example: 由 1 加 到100，用 Matlab 一行就可以了
sum([1:100])
完全不需迴圈
一、各種程式語言寫程式共通的原則
(1) 能夠不在迴圈內做的運算，則移到迴圈外，以節省運算時間
(2) 寫一部分即測試，不要全部寫完再測試 (縮小範圍比較容易 debug)
(3) 先測試簡單的例子，成功後再測試複雜的例子
二、Matlab 寫程式特有的技巧

## Slide 20
三、一些重要的 Matlab 指令
(1) function: 放在第一行，可以將整個程式函式化
(2) tic, toc: 計算時間
tic 為開始計時，toc 為顯示時間
(3) find: 找尋一個 vector 當中不等於 0 的entry 的位置
範例：find([1 0 0 1]) = [1, 4]
find(abs([-5:5])<=2) = [4, 5, 6, 7, 8]
(因為 abs([-5:5])<=2 = [0 0 0 1 1 1 1 1 0 0 0])
(4)  : Hermitian (transpose + conjugation)， .  : transpose
(5) imread: 讀圖， image, imshow, imagesc: 將圖顯示出來，
(註： 較老的 Matlab 版本 imread 要和 double 並用
A=double(imread(‘Lena.bmp’));
(6) imwrite: 製做圖檔

## Slide 21
(7) xlsread: 由 Excel 檔讀取資料
(8) xlswrite: 將資料寫成 Excel 檔
(9) aviread: 讀取 video 檔
(10) dlmread: 讀取 *.txt 或其他類型檔案的資料
(11) dlmwrite: 將資料寫成 *.txt 或其他類型檔案