## Slide 1
Homework 1 (Due: March 28th)
(1) Design a Mini-max lowpass FIR filter such that (40 scores)
 Filter length = 19,  Sampling frequency fs = 3000Hz,
 Pass Band 0~675Hz  Transition band: 600~750 Hz,
 Weighting function: W(F) = 1 for passband, W(F) = 0.5 for stop band .
 Set  = 0.0001 in Step 5.
紙本上要有
(a) the Matlab program, (b) the frequency response,
(c) the impulse response h[n], and (d) the maximal error for each iteration.
0 Hz
600 Hz
675 Hz
750 Hz
※ Matlab program 要 E-mail 電子檔給我 ，E-mail 主旨上註明學號

## Slide 2
(2) (a) What are the two most important applications of the Fourier transform? (b) From the view point of implementation, what are the disadvantages of the discrete Fourier transform? (15 scores)
(3) In IIR filter design, why the step invariant method and the bilinear transform method can reduce the aliasing effect? (10 scores)
(4) (a) Why  the transition band and  the weighting function are important in Minimax FIR digital filter design? (10 scores)
(b) Can the transition band and the weighting function be applied for the MSE FIR digital filter design? (5 scores)
(5) Estimate the length of the digital filter if both the passband ripple and the stopband ripple are smaller than 0.01, the sampling interval Δt = 0.0001, and the transition band is from 500Hz to 600Hz. (10 scores)
(6) Suppose that x[n] = y(0.0001n) and the length of x[n] is 30000. If X[m] is the FFT of x[n] , which frequency components do (a) X[1200] and (b) X[27000] correspond to? (10 scores)